## Slide 1: Pre-Inspection Briefing Guidelines SCHED2 Regime
Notes: A Pre-Inspection Briefing (PIB) should be provided by facility representatives (not by the National Authority / government personnel) and last no more than three hours, though one hour is usually sufficient. Hardcopies are very helpful. The PIB should focus on the necessary site-specific issues, which will be explained in this presentation.

## Slide 2: Initial Disclosure
The Pre-Inspection Briefing (PIB) is the first official activity at the inspected plant site, in a Chemical Weapons Convention (CWC) inspection. Therefore, it is critical that a cooperative atmosphere is created.
This PIB guideline is intended for use by industrial facilities subject to Article VI inspections under the CWC. It serves the Inspected State Party to prepare a thorough, relevant and accurate technical briefing about the facility. That information provided is instrumental to develop inspection plans, helping the Inspection Team fulfil the aims of the inspection mandate in an efficient and timely manner.
The guideline lays out basic requirements in PIB, including operational activities, safety measures, logistics, confidentiality, administration, and other site-specific information, among others.

## Slide 3: General requirement
This guideline is recommended to the Inspected State Party as reference only
The PIB should be provided by facility representatives and conducted no more than 3 hours in length (as per CWC, VA, Part II, paragraph 37)
The PIB presentation can be provided in various forms (e.g., PPT, projection, hardcopy). Hand-outs of the material presented during the PIB are recommended to be provided to the Inspection Team prior to the PIB.
Any site and/or process diagrams could be handed as a separate print-out document from the PIB. This would provide the plant site and the host team better control over such documents during inspection activities.
The Inspection Team will return all the PIB material at the end of the inspection

## Slide 4: A. Introductions of participants
Host team
  Names and functions
Plant/Plant site personnel
  Participants names and functions
Notes: Although the information on this slide is optional, it is recommended introductions to ensure all parties involved in the inspection are introduced to their counterparts and to ensure names and titles are properly referenced in the inspection report. The slide should include the names and positions of the Government Host Team (HT), and plant site representatives participating in the inspection.
The OPCW inspectors will be identified in the host team notification could be sent to the plant site prior to the inspection and also by the Advance Team (AT) (if applicable).

## Slide 5: B. General Information
Brief history of the company and basic information
Type of industry (e.g., fertilizers, pharmaceuticals, pesticides, plasticizers, paints, soaps, etc.)
Management, organization, operations, environment
Certificates of accreditations (e.g., ISO, FDA, etc.)
Security features (e.g., fence/wall, CCTV, patrols, others)
Notes: In case of operational control changes over the recent years further explanation is welcomed.

## Slide 6: B. General Information
  Any changes in the facility (operational, organizational) since the last inspection (if applicable)
  Number of employees
Aerial view map indicating:
    Location in relation to Point of entry (POE)
    Distance from POE
Facility layout indicating:
    Boundaries and gates
    Total area of the plant site

## Slide 7: C. Plant Site Safety Measures
Related to inspection conduct:
  No operation/touching of equipment
  Need for escort
Related to facility:
  Safety hazards and safety procedures
  Specific personal protective equipment
  Emergency alarms and response procedures
  Evacuation routes
  Assembly points
  Location of medical facilities
Notes: This slide informs the inspection team of the site-specific operational safety guidelines governing activities on-site including personal protective equipment requirements for visitors, safety procedures, and training. You may choose to augment the next few slides with any existing safety briefings and/or videos you routinely use to orient and inform visitors to your plant of safety considerations and preparations.
It can also include any safety requirements or restrictions specific to the declared plant(s) and production areas that the inspection team may visit during the inspection activities. This information is provided for the safety of all inspection participants, and also to explain in advance any restricted access measures that will be implemented due to safety concerns. Other common safety measures (i.e., handrails, cell phone restrictions, etc.) should also be included.

## Slide 8: D. Logistics & Administrative Information
Working hours: administration and operations
Working spaces
  Inspectors and escort team working spaces (offices), and briefing areas
  Set-up inspection team office (lockable, power supplied, available during the entire inspection, equipped with desks and chairs)
Communications/Mobile phone policy
Transportation
Lodging and meals
Security and badging procedures
Notes: Administrative and logistics information enables the IT to create an inspection plan that is consistent with the plant site's operational considerations. Plant site working hours should be noted (especially if administrative and operational hours differ). Also, on-site transportation arrangements (primarily if the plant site is large), locations for general discussions, inspection team and host team work spaces, as well as other site specific logistical and administrative requirements should be included in this slide. The plant site should use this slide to reinforce that inspectors will always be accompanied by a host team escort and a plant site representative (if required) while on-site.

## Slide 9: E. Physical Layout
  Provide Plant Layout or comprehensive list indicating the following:
  Declared Schedule 2 plant(s)
  Schedule 3 and DOC/PSF plant(s) (if any)
  Common infrastructure (e.g., QC/R&D laboratories, waste treatment, maintenance, warehouses, pilot plants, medical facilities, etc.)
  Non-declarable plants (e.g., formulation, polymers, inorganic chemicals, etc.)
  Other companies / plant sites which may be physically located within the same boundary, but may not (operationally) form part of the inspected facility
  GPS reading point (if coordinates declared)
Notes: To geographically orient and inform the inspectors, it is helpful to identify major elements, operations, areas and buildings within your fence line, and the boundary of the declared plant site whether coterminous with your fence line.
It is recommended that any site diagrams be handled as a separate print out document from the PIB. This provides the plant site and the host team better control over such documents during inspection activities.

## Slide 10: F. Detailed info – Quantitative Information
Declaration figures (indicate any changes /discrepancies in relation to the declared data)
  Identification of Schedule 2 plant(s) (e.g., building/structure, location, etc.)
  Main activities of Schedule 2 plants [expressed in terms of PGC, Click HERE]
  Activities in relation to Schedule 2 chemicals [Production (PROD) Processing (PROC), Consumption (CONS)]
  Characteristics of the plant(s) [Dedicated, Multipurpose]
  Other activities [expressed in terms of codes B04, B05, B06]
  Production capacity & method of calculation, if applicable
  Specific information in each Schedule 2 chemical [IUPAC/Trade names]
Notes: This slide should reflect the information provided in your data declaration and should point out any changes or amendments identified since submission of the declaration.
Please follow requirements under Part VII of the VA and declaration forms for Schedule 2 regime.

## Slide 11: G. Overview of declared S2 activities
Consider inclusion of the following for each Schedule 2 plant:
  Chemical PROD, PROC, CONS quantities (e.g., annual summary)
  Types of chemical reaction(s) with reaction schemes/process diagrams, (including downstream processes, e.g., filtration, distillation, centrifugation, etc.)
  Materials of construction (e.g., SS, CS, Hastelloy, etc.)
  Mode of operation: Batch/continuous
  Dedicated/multipurpose
  Type of control (e.g., manual, automatic, etc.)
  Associated infrastructure (e.g., tank farms, laboratories, etc.)
  Specific safety features (e.g., detectors, PPE)
List all Scheduled chemicals on the plant site, even if under threshold levels
Notes: In general, an overview of declared activities is provided to clarify the relationship between declared chemicals and chemicals present at the plant site.
Information regarding other scheduled chemicals on-site and DOCs are included to enhance transparency of other activities conducted at the site and to help demonstrate the absence of prohibited activities by identifying potential precursor chemicals present on the plant site.

## Slide 12: H. Records to be reviewed
The records review process is not part of the PIB and therefore these documents should not be included in the PIB material.
It’s highly recommended to have these documents ready at the beginning of the inspection, to optimize the inspection process.
The following is a non-exhaustive list of relevant records generally requested and accessed by the Inspection Team during the records review process

## Slide 13: List of relevant records
Record name | Purpose
Certifications (e.g., ISO)& Business Registration documentation | Verify name, owner, and address of the plant site
Annual/monthly summaries in relation to (PROD,PROC,CONS, Import, Export) | Verify the level of declared activities, non-diversion
Batch records/Daily inventory data/On-screen data | Cross checking to confirm the integrity of the recording system
Complete list of chemicals handled on site | Absence of Schedule1 and undeclared Schedule chemicals and activities
Waste analysis/emission analysis | Non-diversion and absence of any Schedule chemicals
COA of Sched 2 | Purity of S2 chemicals
Notes: The following list of non-exhaustive records is generally accessed by the Inspection Team during the records review.
Consider having these documents ready at the beginning of the inspection, to optimize the inspection process.

## Slide 14: List of relevant records
Record name | Purpose
Technical data (SDS, basic chemistry) | Identify chemical structure, composition of a mixture
Explanation for discrepancy, if any | Identification of causes (Calibration related, S2 chemical destruction)
Methodology for recording systems | Confirm the process of data capturing and register
Notes: The following list of non-exhaustive records is generally accessed by the Inspection Team during the records review.
Consider having these documents ready at the beginning of the inspection, to optimize the inspection process.

## Slide 15: I. Mass Balance - Example
It is recommended that the ISP perform MB calculation in advance. It helps identify potential issues and prepare the rationales (Click HERE for instruction)
Notes: Inspection Team will use this table to verify non-diversion of Schedule 2 chemicals for each Schedule 2 chemical declared.
The plant site can compare the information before the inspection.
Via the hyper link, ISP is able to access to training materials (presentation, instruction paper), which illustrate the use of the table in different case study scenario.

## Slide 16: J. List of acronyms
Acronym | Definition
CWC | Chemical Weapon Convention
DOC | Discrete Organic Chemicals
ISP | Inspected State Party
PIB | Pre-Inspection Briefing
PPE | Personal Protection Equipment
PSF | An unscheduled discrete organic chemical containing the elements phosphorus sulfur or fluorine
VA | Verification Annex
POE | Point of Entry
CS | Carbon Steel
SS | Stainless Steel
OCPF | Other Chemicals Production Facility
SDS | Safety Data Sheet
PGC | Product Group Code

## Slide 17: References
Please refer to the links below for further examples and guidance on how to prepare a PIB
USA National Authority
https://www.cwc.gov/inspections_briefing_overview_text.html#topicFour
UK National Authority
https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/558885/OPCW_Inspection_Guidance__2016_.pdf